## Slide 2
Recommendation: validate before selling. Run a 30-car hydrogen retrofit pilot in a captive Faridabad fleet and scale only if delivered hydrogen falls below about ₹190 per kg
The brief asks whether retrofits can be a safe, affordable, viable complement to BEVs by 2030. Evidence answer: safe with engineering, not affordable at unsubsidised hydrogen prices, viable only as a station-limited niche.
H₂-SHIFT
Convert. Don't Replace.
Stations, not demand, set the niche: bottom-up funnel to 2030 (model)
CNG vehicles on road, Mar 2025
8,195,000
Passenger cars (estimate, 55 percent)
4,507,250
Factory-fitted, boot bay, under 6 yr in 2028
2,253,625
In commercial or institutional fleets
450,725
In cities with a hydrogen hub by 2030
180,290
Early adopters, return-to-base (hypothesis)
9,014
Station-limited capacity: 8 hubs x 174 cars
1,394
Realistic converted fleet, 2030
1,394
Bar length on a log10 scale (1,000 to 8.2 million). One 500 kg/day hub at 70 percent utilisation serves 174 cars at 2.0 kg per car per day; demand (9,000) exceeds station capacity (1,394) sevenfold. Round 1 said 1,00,000 cars.
SAFE: yes, with engineering
Composite cylinder, thermal relief, twin sensors, lean burn with NOx control. No approval route exists for a hydrogen retrofit today: gate 1.
AFFORDABLE: not by 2030
₹13.7/km converted vs ₹5.2/km on CNG at ₹800/kg (2028). CNG fuel parity needs ₹188/kg; cheapest 2030 forecast about ₹360/kg.
COMPLEMENT: niche only
A compact BEV costs ₹5.6/km including purchase. Hydrogen retrofits fit captive fleets beside hydrogen hubs, about 1,400 cars by 2030.
Initial customer and use case
Donor
Maruti Suzuki Dzire Tour S CNG, 3 to 5 years old, factory bi-fuel; petrol stays as automatic backup
Fleet
Captive, return-to-base institutional and contract fleets: PSU and corporate staff transport, airport contracts
Duty
150 to 210 km per day, 330 days; two depot fills per day give about 120 km on hydrogen
Location
Faridabad, Delhi-NCR: IOCL R&D hydrogen dispensing point and the MNRE Sahibabad-Faridabad-Delhi corridor (sanctioned Mar 2025)
Excluded
Delhi app-cabs: aggregator scheme counts only EVs; CAQM allows only CNG or EV new aggregator cars from Jan 2026
Second hub
Ahmedabad-Vadodara-Surat corridor; Gujarat funds 30 percent of the first 20 hydrogen stations
Decision metrics (model, 2028 decision, 5 years)
₹13.7 vs 5.2 vs 5.6
per km: retrofit vs stay on CNG vs BEV (levelised, all-in)
₹188/kg
delivered hydrogen price for fuel parity with CNG
61 km
per hydrogen fill (1.12 kg usable); 555 km petrol backup
~1,400 cars
conditional 2030 fleet, station-limited (Round 1: 1,00,000)
Conditions for success and where they stand today
Retrofit approval route defined (gate 1, Mar 2027)
None exists; AIS-195 covers new vehicles only
Gap
Delivered hydrogen at or below ₹250/kg by 2030 with a path to ₹188
Model hub ₹584; CEEW central ₹360
Not met
Certified kit at or below ₹2.5 lakh installed
₹3.2 lakh at 10,000/yr; ₹7.7 lakh pilot
Not met
NOx at or below 60 mg/km on the BS-VI cycle
Lean burn plus NOx trap provision; not yet tested
Target
Three fleets willing to accept 48 percent power loss and a smaller boot
No interviews yet; Phase 0 buys 30
Hypothesis
What changed since Round 1
Fallback fuel
petrol already fitted, not a second CNG cylinder
Price basis
pump price (₹584 to 1,433/kg), not production cost (₹160 to 200)
Rollout
3 prototypes, 30 pilot cars, about 1,400 by 2030, not 1,00,000
Stop rules
four gates with proceed, redesign or stop criteria
Sources: PNGRB citing Vahan, 81.95 lakh CNG vehicles [W3-S2]; Delhi aggregator scheme [W3-S17]; CAQM direction [W3-S19]; IOCL Faridabad [W3-S46]; MNRE corridors, PIB 3 Mar 2025 [W3-S36]; Gujarat policy [W4-S76]; CEEW 2025 [W4-S22]; workbook sheets Market, TCO, Energy_Range.
2

## Slide 3
Technology choice: H2-ICE is the only route that is a retrofit in cost and scope, but its fuel economics are the weakest; a fuel-cell conversion costs as much as a new BEV
Matched criteria for the same donor and duty: Dzire Tour S CNG, 55,000 km per year, owner decision in 2028. Model outputs unless a source ID is given; estimates are labelled.
H₂-SHIFT
Convert. Don't Replace.
Criterion | H2-ICE retrofit (selected) | Fuel-cell conversion | New compact BEV, donor sold | Continue on CNG
Scope of change | Cylinder, lines, injectors, ECU, sensors; engine and petrol system retained | Whole powertrain: stack, battery, motor, inverter, cooling, tank, controls | New vehicle; donor sold for about ₹3.5 lakh | None
Cost to the owner, 2028 | ₹3.2 lakh installed at 10,000/yr (₹7.7 lakh pilot) | ₹15 to 25 lakh pilot; ₹8 to 12 lakh at volume (estimate, W4) | ₹10.5 lakh (Tiago EV to Punch EV class) [W3-S27] | ₹0
Energy cost per km, 2028 | ₹12.0 blended; hydrogen km ₹14.8 at ₹800/kg | About half of H2-ICE per hydrogen km (stack efficiency) | ₹1.5 at ₹6 depot, ₹20 public per kWh | ₹3.6 at ₹87/kg
All-in cost per km, 5 years | ₹13.7 | Not modelled (capital above BEV) | ₹5.6 | ₹5.2
Range per fill or charge | 61 km on hydrogen plus 555 km petrol | About 2x H2-ICE on the same tank | 187 to 260 km, real-world tests [W3-S30] | About 250 km at 25 km/kg
Refuel or recharge time | 3 to 5 min, 350 bar non-cooled fill | 3 to 5 min | About 1 h DC 10 to 80 percent; 6 to 8 h AC | 3 to 5 min plus queue
Peak power vs petrol | About 52 percent, lean burn (city duty) | Restored by electric drive | Higher | About 85 percent
Tailpipe | Zero CO2 on hydrogen km; NOx must be controlled | Water vapour only | Zero | About 105 g CO2/km
Approval route today | None for retrofits; AIS-195 covers new H2-ICE vehicles | None; AIS-157 scope excludes retrofitted FCEVs | Established | Established
Supplier readiness | Injectors, valves, regulators production-intent; car-size cylinders scarce | Imported stacks; no light-duty supply chain in India | Mature | Mature
Global deployments: what is real, and the lesson
Toyota Mirai (FCEV car)
US sales 210 in 2025; fuel credits needed [W3-S51]
Commercial
Hyundai Nexo gen 2 (FCEV)
Korea only at scale, subsidy-dependent [W3-S52]
Commercial
Toyota hydrogen HiAce (H2-ICE van)
Depot fuelled; under 200 km; SCR for NOx [W3-S55]
Pilot
Suzuki-AVL hydrogen Swift (H2-ICE car)
1.4 L DI, 100 kW, Vienna May 2026; not a retrofit
Prototype
KEYOU truck conversions (H2-ICE)
Only commercial retrofit model; Daimler 2027 [W3-S61]
Pilot
JCB hydrogen engine (off-highway)
EU type approval May 2025 [W3-S60]
Approved
Stellantis hydrogen vans (FCEV)
Cancelled Jul 2025: infrastructure, capital [W3-S64]
Withdrawn
Shell CA, H2 Mobility DE car stations
43 car stations closed 2024 to 2025 [W3-S65, S66]
Withdrawn
Status: Prototype = demonstrator; Pilot = fleet trial with data; Commercial = product on sale; Withdrawn = programme or stations closed.
Why the selected route fits the donor, the customer and the question
Donor fit
1.2 L four-cylinder SI engine with CNG-hardened seats, a 55 L cylinder bay and a 37 L petrol tank: only the fuel system is new; engine, gearbox, body and petrol backup are retained.
Customer fit
Return-to-base duty with two depot fills makes a 61 km hydrogen range workable for 73 percent of a 167 km day; petrol covers the rest, so no car is stranded by a missing station.
Economic fit
The only route whose cost is a kit (₹3.2 lakh) rather than a vehicle (₹8 to 25 lakh). Its case rests on one variable, the delivered hydrogen price, which the pilot is built to measure.
Sources: Donor_Tech and TCO sheets; fuel-cell conversion cost is an estimate from stack and battery cost literature [W4]; BEV data [W3-S27, S30]; AIS-157 scope [W2-S11, Scribd copy]; programmes [W3-S51 to S66]; Suzuki-AVL Swift (Fuel Cells Works, RushLane, May 2026).
3

## Slide 4
Retrofit engineering: storage, fuel delivery, controls and safety are new; the engine, petrol system and body are retained. One fill gives about 61 km; power falls by about half
Donor: Maruti Suzuki Dzire Tour S CNG, 1.2 L K-series, 60 kW on petrol, 55 L steel CNG cylinder in the boot, 37 L petrol tank, 163 mm ground clearance. Concept schematic, not validated CAD.
H₂-SHIFT
Convert. Don't Replace.
Added (new hydrogen parts)
Retained
Modified
Removed
Side view, not to scale; dashed = control link
Engine bay
Cabin
Boot
Engine 1.2 L, gearbox, catalyst (retained)
Injectors, rail
Reg.
H2 ECU
Petrol tank 37 L (retained)
60 L H2 cylinder 350 bar
CNG 55 L removed
NOx trap
Cold plugs, crankcase ventilation and lean calibration with retarded spark (modified)
Hydrogen ECU: dual map, lambda 1.6 to 2.2, automatic petrol fallback, diagnostics (added)
Twin hydrogen sensors in boot and engine bay; vent fan, cabin warning (added)
60 L composite cylinder (OD 400 mm, 767 mm, 36 kg, 1.45 kg H2) with on-tank valve and TPRD; replaces the 55 L steel CNG cylinder; frame to 20 g / 8 g (added)
Engine, gearbox and catalyst retained; injectors and rail on the intake (added)
Two-stage regulator, 350 bar to injection pressure (added)
316L high-pressure line under the floor; lean NOx trap provision on the exhaust (added)
Petrol tank and injection retained, 555 km backup; boot bulkhead sealed and vented (modified)
H35 receptacle with check valve (added); TPRD vent routed outside (added)
The central trade-off: lean burn buys low NOx at the cost of power
Chart: Air-fuel ratio, lambda
| 1.0 | 1.3 | 1.6 | 2.0 | 2.4 | 2.8
Power vs petrol (fraction) | 0.8 | 0.72 | 0.62 | 0.5 | 0.42 | 0.36
Engine-out NOx vs stoichiometric (ratio) | 1 | 2.7 | 1.2 | 0.15 | 0.03 | 0
Schematic curves through literature anchors, not measured data: port injection loses about 20 percent power at lambda 1 and a further 35 to 40 percent at lambda 2 [W1-S9a, S9b]; NOx peaks near lambda 1.3 at about 2.7 times the stoichiometric value and falls to near zero above lambda 2 to 2.7 [W1-S9h, S9b]. Accelerations leave the lean window, hence the NOx trap provision [W4-S70].
Packaging consequences (concept, mock-up in Phase 0)
Item | CNG today | Hydrogen | Effect
Cylinder OD x length | 316 x ~900 mm | 400 x 767 mm | Boot loses ~50 L more
Cylinder mass | ~55 kg steel | 36 kg composite | Kerb mass -13 kg
Fuel on board | ~9 kg CNG | 1.12 kg usable H2 | 35 percent of energy
Seats / luggage | 5 / ~200 L | 5 / ~150 L | Two bags become one
Consumption cross-check (kg H2 per 100 km)
Vehicle | kg/100 km | Basis
This retrofit, fleet use (model) | 1.85 | 0.87 x CNG efficiency at 25 km/kg
Ford Focus H2RV (2.3 L, hybrid) | 1.4 | claimed, 2003 [W1-S12c]
Mazda RX-8 Hydrogen RE, rotary | 2.4 | claimed, 2006 [W1-S12b]
Toyota hydrogen HiAce (3.4 L van) | 3.1 | 6.2 kg for 200 km [W1-S12e]
1.12 kg
usable H2 per fill (1.44 kg nominal, 85 percent fill, 20 bar residual)
61 km
per fill at 1.85 kg/100 km; 105 km at 700 bar
~121 km
per day on hydrogen with two depot fills (73 percent of a 167 km day)
42 PS
peak in hydrogen mode, 48 percent below petrol; petrol switch at high load
-13 kg
net kerb mass; payload unchanged
~150 L
boot left (about 200 L with CNG); seats unchanged
3 days
conversion downtime per car (14 labour hours at volume)
What cannot be reused, and the injection choice
Removed, not reusable: the 55 L steel CNG cylinder (ISO 11439 steels are limited to 2 percent hydrogen), CNG regulator, rail, injectors, hoses and lines. Hydrogen parts need UN R134 or ISO 19881 class qualification [W1-S11a].
Port injection timed after intake-valve closing prevents backfire and pre-ignition but costs power; direct injection (Suzuki-AVL Swift prototype) recovers it but is not a retrofit. Durability to prove: valve seats and guides, lubricant ash, sensor drift.
Sources: Maruti Suzuki Tour S and Dzire specifications [W1-S3a to S3c]; Luxfer G-Stor Pro V060H35 [W1-S2]; hydrogen densities [W1-S13a]; PFI power loss and NOx behaviour [W1-S9a, S9b, S9h]; ISO 11439 limit [W1-S11a]; UN R110 loads [W1-S14d]; Energy_Range and BOM sheets.
4

## Slide 5
Safety and approval: each hazard has a known prevention, detection and test; the unresolved item is approval, because no route exists yet for a hydrogen retrofit of a car
Hydrogen: flammable from 4 to 75 percent in air at 0.017 mJ, diffuses 3.8 times faster than natural gas, burns almost invisibly [W2-S43, S44]. Different risks, not automatically higher, if designed for.
H₂-SHIFT
Convert. Don't Replace.
Hazard | Prevention (design) | Detection and response | Evidence required | Evidence type
Leak into boot, cabin, garage | Sealed bulkhead, vented boot, no ignition sources in the bay, valve closed with ignition off | Two sensors (1 and 2 percent), tank valve closes within 1 s, switch to petrol, cabin warning | Below 4 percent in cabin, below 8 percent at vents (GTR 13 / AIS-195); parked enclosed-space test | Type test
Embrittlement, permeation, ageing | 316L lines, hydrogen elastomers, composite liner; no CNG steel parts reused | Leak check at service; 3-yearly requalification; 15-year life | ISO 19881 / UN R134 supplier qualification; cycling and permeation | Standard
Crash damage | Cylinder inside the crush-free zone; frame to 20 g / 8 g | Inertia switch closes the tank valve; post-crash leak limit | Sled test; full-vehicle rear crash under AIS-195 | Type test
Overpressure and fire | TPRD vents away from occupants and wheel wells; burst ratio 2.25 x NWP | TPRD opens on heat: controlled release, not rupture | Bonfire, burst, drop, cycling (GTR 13); vent-routing review | Type test
Detection or control failure | Redundant sensors, ECU watchdog, manual shut-off, limp-home on petrol | Fault codes, forced petrol mode, service lock-out | Fault injection and hardware-in-the-loop; 500 h engine durability | Programme test
Workshop and refuelling | NFPA 2 ventilation (1 cfm per sq ft), detection, permit-to-work, PESO-trained staff | Dispenser and bay interlocks; nitrogen purge for venting | PESO Form-H licence; SAE J2601 fill protocol; incident drills | Licence
Combustion emissions (NOx) | Lean burn lambda 1.6 to 2.2, retarded spark, NOx trap provision, load limiting | Lambda sensor and OBD | BS-VI 60 mg/km on the certification cycle; quarterly pilot tests | Target
Approval sequence: what exists and what is missing
1
New-vehicle hydrogen ICE standard
AIS-195:2023 (Amd 1, May 2025) via CMVR Rule 125M, GSR 746(E) [W2-S13]
Established
2
Retrofit gateway in law
MV Act s.52; Rule 126 proviso; Rule 115 kit machinery written for CNG and LPG [W2-S3, S9]
Established
3
Hydrogen retrofit kit standard and emission procedure
None; AIS-157 excludes retrofitted FCEVs; AIS-195 retrofit position unverifiable [W2-S11]
Gap
4
Car-size cylinder approval (PESO)
Gas Cylinder Rules 2025 cover on-board hydrogen; only 150 to 250 L truck cylinders approved [W2-S24, S30]
Unresolved
5
Dispensing licence
PESO Form-H online since May 2025; SMPV(U) 2025 for bulk storage [W2-S27]
Established
6
Registration, insurance, warranty
Form 22D endorsement needs an approved kit; IMT-25 covers CNG/LPG only; OEM warranty void [W2-S53, S54]
Unresolved
7
Trial route for the pilot
Trade certificate plus test-agency evaluation (Mirai 2022, Tata trucks 2025); MNRE scheme names 4-wheelers
Established
NOx is the emission that matters: hydrogen combustion still forms thermal NOx (US DOE [W2-S52]). Lean burn above lambda 2 is near zero at steady state, but accelerations leave that window, so the kit carries a lean NOx trap provision and gate 2 requires 60 mg/km or better on the BS-VI cycle. Target, not a result. No 'approved' or 'fully safe' claim is made; safety evidence comes from type tests and standards, not from incident-free pilot operation.
Gate 1 (March 2027): a written regulator and test-agency view on the retrofit route, or the programme stops. Legend: green = in force; amber = exists but not for this case; red = missing instrument.
Sources: H2Tools and DOE properties [W2-S43, S44]; NFPA 2 [W2-S45]; GTR 13 limits [W2-S42]; GSR 746(E) [W2-S13]; Rules 126 and 115 [W2-S9, S3]; AIS-157 scope [W2-S11]; Gas Cylinder Rules 2025 [W2-S24]; Form-H [W2-S27]; IMT-25, Form 22D [W2-S53, S54]; incidents [W2-S48, S49].
5

## Slide 6
Economics: over five years the converted car costs the owner ₹16.8 lakh more than staying on CNG and ₹16.2 lakh more than switching to a BEV; fuel is the whole story
Fair comparison for an owner deciding in 2028 with a 3-year-old Dzire Tour S CNG. Same horizon, mileage, discount rate and time costs; donor sale credited to the BEV option; residual values credited to all.
H₂-SHIFT
Convert. Don't Replace.
Five-year cost of ownership by category, ₹ lakh NPV (model, base case)
Chart: ₹ lakh, present value at 12 percent
| Continue on CNG ₹10.4 lakh, ₹5.2/km | Hydrogen retrofit ₹27.3 lakh, ₹13.7/km | Sell, buy compact BEV ₹11.0 lakh, ₹5.6/km
Capital net of residual value | -0.57 | 2.66 | 4.92
Fuel or energy | 7.64 | 21.01 | 3.15
Maintenance and tyres | 1.79 | 1.99 | 0.99
Insurance and inspection | 0.67 | 0.9 | 1.08
In-shift time cost | 0.89 | 0.71 | 0.89
₹ lakh | CNG | H2 | BEV
Capital net of residual | -0.6 | 2.7 | 4.9
Fuel or energy | 7.6 | 21.0 | 3.1
Maintenance, tyres | 1.8 | 2.0 | 1.0
Insurance, inspection | 0.7 | 0.9 | 1.1
In-shift time | 0.9 | 0.7 | 0.9
Total NPV | 10.4 | 27.3 | 11.0
₹ per km | 5.2 | 13.7 | 5.6
Colours match the chart segments. Capital is net of residual value (negative for the kept CNG car). Petrol backup km are inside 'fuel or energy' for the retrofit (₹5.0 lakh).
Fuel or energy: hydrogen km ₹14.8/km at ₹800/kg falling 10 percent a year, petrol backup km ₹6.8, CNG ₹3.5, BEV ₹1.5. Negative capital for the CNG car is its residual value.
Conversion cost by category, ₹ lakh installed (BOM sheet)
Chart: ₹ lakh
| Pilot batch ₹7.7 lakh | 10,000 per year ₹3.2 lakh
Storage and mounting | 3.35 | 1.24
Fuel delivery | 1.46 | 0.46
Controls and safety | 0.67 | 0.22
Engine and NOx provision | 0.43 | 0.19
Installation and testing | 0.34 | 0.11
Certification allocation | 0 | 0.08
Warranty, margin, GST | 1.49 | 0.93
Category | Pilot | Volume
Storage and mounting | 3.35 | 1.24
Fuel delivery | 1.46 | 0.46
Controls and safety | 0.67 | 0.22
Engine and NOx provision | 0.43 | 0.19
Installation and testing | 0.34 | 0.11
Certification allocation | 0.00 | 0.08
Warranty, margin, GST | 1.49 | 0.93
Installed total incl. GST | 7.74 | 3.22
Extra cost vs staying on CNG, ₹ lakh over 5 years
₹/kg \ km/yr | 30,000 | 50,000 | 70,000
₹150 | +3.6 | +3.8 | +4.0
₹250 | +4.7 | +5.6 | +6.5
₹400 | +6.3 | +8.3 | +10.3
₹600 | +8.5 | +11.9 | +15.4
₹800 | +10.7 | +15.6 | +20.5
Every cell is positive: no cell turns negative in the workbook grid down to ₹100/kg. More mileage widens the gap while hydrogen is above ₹188/kg.
Break-even indicators (model)
CNG fuel parity
₹188/kg delivered
Petrol fuel parity
₹368/kg
Full-TCO break-even vs CNG
none in 5 years at any price
Full-TCO break-even vs BEV
none at base; needs about ₹150/kg, ₹2 lakh kit, 85 percent hydrogen km
Abatement cost vs CNG
₹129,000/t CO2e at base; about ₹45,000/t at ₹250/kg (credits ₹1,350 to 2,800/t)
Assumptions used in every exhibit on this slide (Inputs sheet; downside and upside cases in the annexure)
Decision 2028, 5 years
55,110 km/yr
Discount 12 percent
H2 ₹800/kg, minus 10 percent/yr
CNG ₹87/kg at 25 km/kg
Petrol ₹102/L
H2 1.85 kg/100 km, 65 percent of km
Power ₹6 depot, ₹20 public per kWh
BEV ₹10.5 lakh, resale ₹4.2 lakh
Donor sale ₹3.5 lakh
Time ₹150/h in shift
Reading: the retrofit is a decarbonisation cost, not a saving. Hydrogen km cost ₹14.8 against ₹3.5 on CNG, and the 35 percent of km on petrol backup add ₹5.0 lakh. It needs a paying counterparty or a cheaper molecule than any 2030 forecast found (CEEW ₹360/kg delivered; refinery-gate record ₹279/kg before compression).
Sources: fuel prices Sep 2026 [W4-S16, S19]; DERC tariff, public charging [W4-S20, S21]; BEV prices, tests, warranties [W3-S27, S30; W4-S26]; NITI Aayog mileage [W4-S30]; CEEW 2025 [W4-S22]; Numaligarh tender [W3-S39]; carbon credits [W4-S73]; TCO, BOM and Sensitivities sheets.
6

## Slide 7
Hydrogen supply: a 30-car pilot needs about 60 kg a day; delivered hydrogen costs about ₹1,433/kg at a pilot point and ₹584/kg at a 2030 hub, and utilisation alone cannot reach parity
Pilot setting: Faridabad, Delhi-NCR (IOCL R&D dispensing since the 2022 Mirai pilot; MNRE corridor sanctioned March 2025, 18 to 24 months to commission). No station is public or confirmed available: access is a proposed partnership.
H₂-SHIFT
Convert. Don't Replace.
Supply-to-fleet flow with pilot quantities (model, H2_Supply sheet) and proposed owners
1. Green hydrogen producer
SIGHT-awarded plant; ₹400/kg at gate (2026-28), ₹240/kg (2030); certified 2 kg CO2e/kg
Producer
2. Tube-trailer delivery
300 kg payload; 1.4 loads per week; ₹45/kg; about 150 km
Logistics contractor
3. Cascade storage
90 kg buffer (1.5 days) at 450 bar
OMC station partner
4. Compression
9.4 kg/h on a 150 kg/day design; 3 kWh/kg
OMC station partner
5. Dispensing (H35)
2 positions; 60 fills/day, 10 per hour in the peak window; PESO Form-H
OMC station partner
6. Fleet consumption
30 cars x 2 fills; 60 kg/day; 65 percent of km on hydrogen
Fleet partner
Delivered price falls with utilisation but never reaches CNG parity (model)
Chart: ₹ per kg delivered
| 20 percent | 35 percent | 50 percent | 65 percent | 80 percent | 95 percent
Pilot point 2028: 150 kg/day, delivered H2 | 2780 | 1818 | 1433 | 1226 | 1096 | 1007
Hub 2030: 500 kg/day, delivered H2 | 1162 | 815 | 677 | 602 | 556 | 524
Petrol fuel parity ₹368/kg | 368 | 368 | 368 | 368 | 368 | 368
CNG fuel parity ₹188/kg | 188 | 188 | 188 | 188 | 188 | 188
At 95 percent utilisation the hub price is still ₹524/kg: production, transport and compression alone (₹312/kg) exceed CNG parity. Station utilisation is the axis; capex ₹10 crore (pilot) and ₹12 crore (hub) recovered over 10 years at 12 percent.
Ownership and risk (proposed, not committed)
Function | Proposed holder | Risk carried
Vehicles | Fleet partner (PSU, corporate or airport contract) | Residual value, backed by programme buy-back
Kits | SRDI-led consortium; kit integrator warrants | Development and warranty
Dispensing point | OMC partner (proposed IOCL, Faridabad), Form-H licence | Utilisation, covered by take-or-pay from the fleet
Fuel | SIGHT-awarded producer by tube trailer | Supply reliability; buffer covers 1.5 days
Service | Two hydrogen-ready workshops; PESO test station | Safety compliance and training
Evaluation | IIT Delhi or CEEW (proposed) | Credibility of results
Delivered price build-up, ₹ per kg (model): pilot point 2028 versus 2030 hub
Component | Pilot point, 150 kg/day at 50 percent | Hub 2030, 500 kg/day at 70 percent
Production at plant gate (green) | 400 | 240
Tube-trailer transport | 45 | 45
Compression electricity | 27 | 27
Station capital recovery (10 years, 12 percent) | 647 | 166
Station fixed O&M | 146 | 38
Losses, margin and taxes | 168 | 69
Delivered price at the dispenser | 1,433 | 584
Main bottleneck: not station throughput (2 dispensers cover 60 fills a day) but the hydrogen price stack. Delivered gas keeps pilot capital to a dispensing point; on-site electrolysis is justified only at hub scale. Petrol backup covers supply interruptions.
Station sizing from the fleet (H2_Supply sheet)
• 30 cars x 167 km x 0.0185 kg/km x 0.65 = 60 kg/day
• 60 fills/day, 50 percent in a 3 h window = 10/h, 2 dispensers
• Compressor 9.4 kg/h over 16 h; buffer 90 kg (1.5 days)
• Cars alone use 40 percent of capacity; 50 percent assumed with bus and truck users
• One 2030 hub serves 174 cars at 70 percent utilisation
Sources: MNRE corridors, PIB 3 Mar 2025 [W3-S36]; IOCL Faridabad [W3-S46, W4-S81]; CEEW station model [W4-S22]; ICCT utilisation [W4-S46]; Indian station capex indication [W4-S56]; green hydrogen cost [W4-S33, S38, S57]; Gas Cylinder Rules, Form-H [W2-S24, S27]; H2_Supply sheet.
7

## Slide 8
Roadmap to 2030: four gated phases across five workstreams, ₹37.6 crore including contingency, with a proceed, redesign or stop decision at each gate
October 2026 to September 2030. Suzuki R&D Center India proposed as engineering lead; public support sought under the MNRE transport pilot scheme, which names buses, trucks and 4-wheelers (PIB 14 Feb 2024).
H₂-SHIFT
Convert. Don't Replace.
2026
2027
2028
2029
2030
Decision gates
Phase and budget (₹ crore)
Phase 0: feasibility ₹0.9 cr
Phase 1: engineering and controlled validation ₹8.5 cr
Phase 2: certification and pilot build ₹15.2 cr
Phase 3: pilot operation ₹8.1 cr
Cond.
G1 Mar 2027
G2 Mar 2028
G3 Mar 2029
G4 Sep 2030
Engineering
Owner: SRDI lead
Packaging mock-up, CAD, hazard analysis
500 h test-cell programme; 3 prototype conversions
30 conversions; installer training
Field support, calibration updates
Testing and approval
Owner: ARAI or ICAT; PESO
Route consultation: AISC, MoRTH, ARAI, ICAT, PESO
Storage qualification; leak, ventilation, crash-structure tests
Kit type approval; 80,000 km durability on 2 cars
Quarterly emission and safety tests
Fuel supply
Owner: OMC partner
Station partner letter; supply options
Supply contract; Form-H application
Dispensing point commissioned
Deliveries 1.4 loads/week; utilisation log
Fleet operations
Owner: Fleet partner
30 interviews; telematics on 20 cars
Driver and workshop training plan
2 workshops upgraded; 30 cars inducted
18 months with 10 CNG and 10 BEV comparison cars
Commercial validation
Owner: SRDI with evaluator
Demand evidence from 3 fleets
Cost model with supplier quotations
MNRE sanction; insurer endorsement
Independent evaluation; scale decision
Dependencies: gate 1 needs the regulator view and a station partner letter; Phase 1 needs car-size cylinder samples (Luxfer, Quantum, NPROXX, Time Technoplast) and hydrogen injectors; Phase 2 needs the MNRE sanction, PESO approvals and corridor station timing; Phase 3 needs the fuel contract and an insurer endorsement. Phase 4 (from Oct 2030, grey) is conditional: 1,000 to 1,500 cars at up to 8 hubs.
Gate | Proceed if | Otherwise
G1 Mar 2027 | Written route from regulator and test agency; station partner secured; demand evidence from 3 fleets | Stop
G2 Mar 2028 | At or below 2.2 kg/100 km; NOx at or below 60 mg/km on cycle; no abnormal combustion in 500 h; safety tests passed | Redesign once, then stop
G3 Mar 2029 | Kit approval granted; dispensing point commissioned within 6 months of plan | Pause
G4 Sep 2030 | Availability 95 percent; zero reportable hydrogen incidents; measured ₹/km published; delivered hydrogen at or below ₹250/kg with a credible path to ₹190/kg | Stop and publish
Proposed funding of ₹37.6 crore (shares are proposals)
40%
35%
15%
10%
SRDI and Maruti Suzuki ₹15.0 cr | Public: MNRE pilot or R&D scheme, state policy ₹13.1 cr | OMC partner ₹5.6 cr | Fleet partner ₹3.8 cr. Why Suzuki's role is plausible: CNG engine and calibration know-how, 70 percent of India's CNG cars, its own hydrogen combustion prototypes (Swift with AVL, Burgman). No endorsement is implied.
Sources: MNRE scheme guidelines, PIB 14 Feb 2024 (buses, trucks and 4-wheelers) [PIB 2006052]; ARAI Phase-II call for proposals (Sep to Dec 2025); test facilities [W4-S14, S15]; CNG kit approval precedent [W2-S3, S8]; PESO rules [W2-S24]; Pilot_Budget sheet.
8

## Slide 9
Impact is real but small by 2030: about 1,400 cars and 3.6 kt CO2e a year, conditional on the gates. The decision requested is ₹0.9 crore for Phase 0
Matched service (same car, same duty) for every comparison; projections are labelled as modelled, pilot target or conditional scenario, never as achieved results.
H₂-SHIFT
Convert. Don't Replace.
Emissions per km, well-to-wheel with manufacturing (model)
Chart: g CO2e per km
| Continue on CNG | Retrofit, green H2 | Retrofit, grey H2 | BEV, 2025 grid | BEV, 2030 grid
g CO2e per km | 137 | 89 | 208 | 176 | 134
Green-hydrogen retrofit is 35 percent below CNG with petrol backup km included; grid-electrolysis hydrogen would be 533 g/km, four times CNG. Reversal: hydrogen above 5.9 kg CO2e/kg makes the retrofit worse than CNG; grid below 0.29 kg/kWh at the meter makes the BEV cleaner (CEA path about 0.5 by 2032). NOx remains.
Scenario table (per car unless stated)
Metric | Baseline: keep CNG | Modelled retrofit, base | Pilot target 2029-30 | Conditional 2030 (about 1,400 cars)
CO2e, g/km | 137 | 89 | at or below 95 | 3,645 t/yr avoided
Hydrogen use | 0 | 1.85 kg/100 km | at or below 2.2 | 924 t/yr demand
Cost per km, all-in | ₹5.2 | ₹13.7 | measured and published | depends on hydrogen price gate
Availability | reference | not yet measured | at or above 95 percent | at or above 95 percent
Pilot scorecard: metric, success threshold, measurement
Metric | Threshold (gate 4) | How measured
Consumption | at or below 2.2 kg/100 km in fleet use | Dispenser mass logs, CAN flow
Range per fill | at or above 55 km | Trip logs, GPS
Hydrogen share of km | at or above 60 percent | Telematics, fuel mode log
Availability | at or above 95 percent | Downtime by cause
Safety | zero reportable incidents; all alarms closed | Incident register, sensor logs
NOx | at or below 60 mg/km on cycle | Test agency, quarterly
Maintenance cost | within ₹1.2/km | Job cards
Refuelling time | under 6 min per fill | Dispenser logs
Delivered hydrogen | at or below ₹250/kg, path to ₹190 | Fuel invoices, station utilisation
Acceptance | fleet managers and drivers accept power and boot | Quarterly interviews, willingness to pay
Major unresolved risks (ranked)
Risk | Why it matters | Mitigation
Delivered hydrogen price | ₹360 to ₹1,430/kg across sources; decides the scale case | Price gate; take-or-pay; pilot fuel as programme cost
Approval route | No instrument for a hydrogen retrofit kit | Gate 1 consultation; trial under trade certificate
NOx on transients | Lean window lost under acceleration | NOx trap provision; load limiting; cycle test at gate 2
Cylinder supply | No car-size PESO-approved cylinder | Samples from 4 suppliers in Phase 0; PESO prototype approval
Customer demand | Hypothesis; power and boot loss may be refused | 30 interviews; gate 1 needs 3 fleets
Decision requested
1
Approve Phase 0: ₹0.9 crore, six months
regulator consultations, 30 fleet interviews, telematics on 20 cars, boot mock-up; no commitment beyond gate 1
2
Endorse a scheme application
MNRE transport pilot scheme, 4-wheeler category, with ARAI as implementing agency; Gujarat station subsidy for the second hub
3
Nominate roles
SRDI engineering lead; fleet and fuel partner shortlist (proposed IOCL Faridabad; PSU and airport-contract fleets)
4
Start HCNG in parallel
where a CGD company blends to IS 17314: legal since 2020, no vehicle change, about 6 percent of energy from hydrogen; an air-quality step
What would make us stop
No written regulator route by March 2027
Backfire or NOx not controlled within 500 test-cell hours
Delivered hydrogen above ₹250/kg in 2030 with no path to ₹190/kg
Fleets refuse the power and boot loss in Phase 0 interviews
H2-SHIFT keeps India's hydrogen retrofit option open at low cost, states the price at which it works, and hands the 2030 scale decision to evidence.
Sources: CEA CO2 baseline v21 and National Electricity Plan [W4-S59, S60]; IPCC fuel factors [W4-S62]; ICCT 2025 lifecycle and battery factors [W4-S63]; hydrogen carbon intensities [W4-S64, S65]; DOE NOx page [W2-S52]; MNRE scheme scope [PIB 2006052]; H-CNG notification [W2-S1]; Emissions, Market and Pilot_Budget sheets.
9

## Slide 10
Key sources by theme (IDs as used on the slides) and annexure index
Research cut-off 14 September 2026. The full register (309 entries with URLs, dates, sections and limitations) is in Annexure A2 and the workbook Sources sheet.
H₂-SHIFT
Convert. Don't Replace.
Policy, standards and approval
• W2-S13 MoRTH GSR 746(E), 16 Oct 2023: Rule 125M, AIS 195:2023 (Amd 1, May 2025)
• W2-S11 MoRTH GSR 579(E), 23 Sep 2020: AIS 157:2020; scope excludes retrofitted FCEVs
• W2-S1 MoRTH GSR 585(E), 25 Sep 2020: H-CNG per IS 17314:2019
• W2-S3, S9 CMVR Rules 115 and 126 (CNG/LPG kit provisions, retrofit proviso)
• W2-S24, S27 Gas Cylinders (Amendment) Rules 2025, GSR 225(E); PESO Form-H licensing (May 2025)
• W2-S42 to S45 UN GTR 13 Amend. 1 (2023); H2Tools and DOE properties; NFPA 2 (2023)
Market, fleet and customer
• W3-S2 PNGRB citing Vahan: 81.95 lakh CNG vehicles (Mar 2025)
• W3-S4, S6 MoPNG: 8,150 plus CNG stations; 17,700 to 18,000 by 2030 (targets)
• W3-S10, S12 Maruti Suzuki CNG sales: 6.12 to 6.2 lakh FY25, above 7 lakh FY26; 71.6 percent segment share
• W3-S17, S19 Delhi aggregator scheme 2023; CAQM NCR direction (Jan 2026)
• W4-S30 NITI Aayog (Feb 2026): 4W taxi mileage 70,000 km/yr
• W3-S27, S30 Tata Tiago EV, Punch EV, Xpres-T prices; Autocar India real-world tests
Vehicle, components and combustion
• W1-S3a to S3c Maruti Suzuki Tour S and Dzire specifications and releases
• W1-S2 Luxfer G-Stor Pro H2 table (V060H35: 60 L, 350 bar, 36 kg, 1.45 kg)
• W1-S1 Hexagon Purus Type 4 cylinder table (Rev 08/22)
• W1-S9a, S9b, S9h PFI air displacement and power loss; lambda-NOx behaviour (IJHE 2024-25; Onorati et al.)
• W1-S11a ISO 11439 hydrogen limit for steel CNG cylinders
• W4-S1, S2 US DOE records 19008 and 24006: Type IV storage system cost
Hydrogen supply and cost
• PIB 2107795 (3 Mar 2025): 5 pilots, 37 vehicles, 9 stations, 10 routes, ₹208 crore
• PIB 2006052 (14 Feb 2024): scheme guidelines, buses, trucks and 4-wheelers, ₹496 crore; W3-S37 PIB 29 Jul 2026: 12 projects, 70 vehicles, 16 stations
• W4-S22 CEEW 2025: delivered green hydrogen USD 4.2/kg in 2030; above USD 10/kg today
• W4-S33, S38, S57 CEEW, SIGHT ammonia auctions, IEA GHR: production cost evidence
• W3-S39 Numaligarh refinery tender ₹279/kg; W4-S46 ICCT station cost by utilisation
• W3-S46, W4-S81 IOCL R&D Faridabad hydrogen dispensing
Emissions
• W4-S59, S60 CEA CO2 Baseline Database v21 (0.710 t/MWh, FY2024-25); National Electricity Plan 2022-32
• W4-S62 IPCC 2006 fuel factors (petrol, natural gas)
• W4-S63 ICCT 2025 lifecycle factors; battery about 70 kg CO2e/kWh
• W4-S64, S65 IEA hydrogen carbon intensities; MNRE Green Hydrogen Standard (2 kg CO2e/kg)
• W2-S52 US DOE: hydrogen combustion and NOx
Global programmes
• W3-S51, S52 Toyota Mirai sales; Hyundai Nexo
• W3-S55, S56 Toyota hydrogen HiAce pilot; GR Corolla H2
• Fuel Cells Works, RushLane (May 2026): Suzuki-AVL hydrogen Swift prototype; W3-S58 Suzuki Burgman
• W3-S59 to S63 Cummins B6.7H India; JCB type approval; KEYOU; MAN; ULEMCo
• W3-S64 to S67 Stellantis (Jul 2025); Shell California (Feb 2024); H2 Mobility Germany (2025); GM-Honda
Annexure index (separate PDF and workbook)
Section | Content
A1 | Claim audit: Round 1 versus evidence, with corrections
A2 | Assumptions, evidence classes, full source register
A3 | Cost model: BOM, TCO cash flows, break-even, sensitivities
A4 | Packaging, energy balance and performance calculations
A5 | Regulatory compliance matrix and hazard analysis
A6 | Market sizing method and funnel
A7 | Global benchmark evidence
A8 | Pilot design, instrumentation, first 90 days
A9 | Phase budgets, responsibilities, funding
A10 | Judge Q&A, validation log, change log
Workbook | H2SHIFT model: 11 formula-driven sheets, recalculated
Model inputs by evidence class (98 inputs)
A 31
B 13
C 52
D 2
A 31 | B 13 | C 52 | D 2 (A verified, B model, C assumption, D target)
Evidence classes: A verified external evidence; B model estimate; C explicit assumption or range; D proposed target. Many originals were inaccessible through the build environment's network policy; entries marked 'excerpt' or 'summary' rest on indexed page text and should be re-verified before external use. No customer interviews, letters of interest, test results or partnerships are claimed.
Team Wookies, NIT Warangal. SRDI Igniters Innovation Challenge 2026, Engineering Track, Option 2: Hydrogen Retrofit Solution. Round 2 submission.
10