## Slide 1
India Chem 2026 Youth Innovation Challenge
NAADI
Early fault detection for critical pumps, on the plant's own network
A six-month pilot to test early fault detection across 25 critical pumps in a mid-sized speciality chemicals plant.
Annexure problem statement: AI-driven predictive maintenance to improve asset reliability and maintenance efficiency in the chemicals and petrochemicals sector [1]
From bearing vibration to a drafted work order
DE
NDE
centrifugal pump with vibration and temperature sensors on both bearing housings
vibration signature, sampled continuously
Area gateway
edge feature extraction
Maintenance alert
bearing wear trend rising: work order drafted for the reliability engineer
Raunak Jain B.Tech Mechanical Engineering
Anushriya Bhattacharya B.Tech Chemical Engineering
National Institute of Technology Warangal
India Chem 2026 · NIT Warangal
1 / 8
Notes: Good morning. We are Raunak Jain, mechanical engineering, and Anushriya Bhattacharya, chemical engineering, from NIT Warangal. Our proposal is NAADI, our response to the predictive maintenance problem statement: an early fault detection system for the critical pumps of a chemical plant. To be precise about the claim: NAADI does not predict the exact moment a pump will fail. It watches vibration continuously, spots developing faults early, and alerts the reliability engineer with a drafted work order, while all data and models stay on the plant's own network. We are proposing a six-month pilot to test exactly that. The base-case economics, a public benchmark validation of our prototype, and the pilot design follow in the next seven slides. About 60 seconds.

## Slide 2
Existing scenario
Twenty-five critical pumps can put nearly ₹1.4 crore of annual production value at risk
Where the risk concentrates
≈200 pumps in the plant
Plant assumption
25 critical bad-actor pumps
Pilot scope
60 outage hours per year
Team estimate
≈₹1.4 crore annual exposure
Team calculation
How ₹1.4 crore is worked out: 60 h × ₹1.9 lakh per hour = ₹1.14 Cr of lost margin, plus 12 repairs × ₹2.5 lakh = ₹0.30 Cr. Team calculation from the labelled estimates [11].
How a routine fault becomes an outage
Bearing or seal degradation begins [8]
Monthly inspection misses the developing fault
Pump trips without warning
Production interruption
Emergency repair and restart
89%
of failure modes in the foundational reliability study for RCM showed no predictable wear-out age [7]
Fixed-interval maintenance cannot anticipate faults that arrive at random. Bearing and seal problems develop over days to weeks [8]; that window is where condition data helps.
What NAADI must do: spot developing faults on these 25 pumps early (the target is two weeks of notice) and alert the engineer with a drafted work order.
60 h/yr
unplanned outage from these pumps
Team estimate
₹1.9 lakh/h
contribution margin lost while down
Team calculation
12 events/yr
pump repairs across the 25 units
Team estimate
≈₹1.4 Cr
annual exposure, margin plus repairs
Team calculation
India Chem 2026 · NIT Warangal
2 / 8
Notes: The use case is one representative mid-sized speciality chemicals plant, and inside it the 25 pumps whose trips actually stop production. The funnel on the left shows the filtering: about 200 pumps, 25 critical ones, an estimated 60 outage hours a year, and roughly 1.4 crore of annual exposure once lost margin and repairs are added. These plant figures are labelled estimates and the pilot's first phase replaces them with the plant's own 24-month history. The middle shows why this keeps happening: monthly inspection rounds leave long blind windows, and the foundational reliability study found 89 percent of failure modes have no predictable wear-out age, so calendar-based maintenance misses them. Bearing and seal problems develop over days to weeks. That is the window NAADI is designed to use. About 70 seconds.

## Slide 3
Global best practices
Continuous monitoring works, but proprietary systems remain difficult for mid-sized plants to adopt
Five approaches, six weighted criteria
Approach | Lead time (30) | Cost (20) | Skill need (10) | Data control (10) | Retrofit (10) | MSME fit (20)
Run to failure | none | poor | low | n/a | n/a | poor
Calendar preventive (common in India) | none for random faults | medium | low | n/a | n/a | medium
Monthly offline vibration rounds | up to route interval | medium | high | plant | good | poor
OEM cloud monitoring | days to weeks | high | low | vendor silo | medium | poor
NAADI: on-site continuous stack | days to weeks | low to medium | medium | plant | good | good
Weights in brackets, sum 100. Marks are team judgement based on the documented behaviour of each approach class [2][5].
Weighted score out of 5
Run to failure
2.3
Calendar preventive
3.0
Offline vibration rounds
2.9
OEM cloud monitoring
2.9
NAADI on-site stack
4.3
The gap is not sensing or algorithms. It is cost, data control and fit for mid-sized plants.
How a score is built: each approach gets a 1-to-5 mark per criterion; the score is the weighted average. NAADI: (5×30 + 4×20 + 3×10 + 5×10 + 4×10 + 4×20) / 100 = 4.3.
Design choices
Continuous sensing
no month-long blind windows
Explainable vibration features
auditable by plant engineers
Plant-controlled data
no vendor silo
Retrofit installation
no shutdown, no cabling
Connection to the existing CMMS
alerts become work orders
India Chem 2026 · NIT Warangal
3 / 8
Notes: We compared five realistic approaches on the six criteria that decide adoption, weighting detection lead time and fit for mid-sized plants highest. Run to failure and calendar-based maintenance give no lead time for random faults, and calendar maintenance is still the common practice in Indian plants. Monthly offline vibration rounds help but leave blind windows of several weeks and depend on scarce analysts. OEM cloud monitoring is the global best practice and it works, but it scores poorly here on total cost and on data control, because the plant's condition history ends up in a vendor system. So the gap is architectural rather than technical. That analysis gives the five design choices at the bottom, and those choices define NAADI. The scores are our judgement and are labelled as such. About 65 seconds.

## Slide 4
Proposed solution
NAADI links vibration sensing to maintenance action while keeping operational data on site
All data and models stay on the plant network
critical pump, DE and NDE sensor points
Vibration + temperature sensors
wireless, on both bearing housings; hardware meeting applicable PESO and IECEx requirements [6]
Area gateway
one per plant area; buffers data locally
Edge feature extraction
16 vibration indicators per window, per ISO 13374 [5]
Anomaly + fault classification
anomaly score and fault type per pump; benchmark on slide 5 [10]; the pilot tests it on real plant data
Reliability dashboard
trends, alarm zones per ISO 20816-3 [5]
CMMS work order
drafted automatically in the plant's existing system
Engineer validation
accepts or rejects every action; nothing is automatic
confirmed maintenance findings retrain the model and tighten alarm limits
Open data protocols
OPC UA and standard historian interfaces; nothing proprietary between plant and models
Interpretable features
every model input is a standard vibration indicator an engineer can check
Human-approved action
no maintenance decision changes without the reliability engineer's sign-off
India Chem 2026 · NIT Warangal
4 / 8
Notes: This is the whole system on one picture. Wireless vibration and temperature sensors sit on both bearing housings of each pump, using hardware that meets the applicable PESO and IECEx requirements for hazardous areas. An area gateway extracts sixteen standard vibration indicators per measurement window, following ISO 13374, and ISO 20816-3 alarm zones give usable limits from day one. The model layer produces a per-pump anomaly score and a fault type. Results feed a reliability dashboard, and each alert arrives as a drafted work order inside the plant's existing CMMS. The reliability engineer approves or rejects every action, and confirmed findings feed back to retrain the model. Everything inside the dashed boundary runs on the plant network, so the condition history stays with the plant. What is genuinely ours is the model layer and the workflow integration; sensors and gateways are mature industrial products. About 70 seconds.

## Slide 5
Technical feasibility
The benchmark result is promising; the plant pilot must now test performance under real operating conditions
Feature pipeline
Raw vibration signal
Windowing
2,048 samples, 0.17 s
16 engineering features
RMS · kurtosis · crest factor · band energy
Random forest
300 trees
Output
fault category + anomaly score
Prototype benchmark results
97.9%
four-class benchmark accuracy, unseen 3 hp load [10]
0 of 237
healthy benchmark windows misclassified [10]
98.9%
grouped cross-validation accuracy [10]
CWRU is a controlled test-rig dataset with seeded faults. These results do not represent proven chemical-plant performance.
Evaluation note: whole recordings and one entire motor load were held out; windows from one recording never appear in both training and test.
Confusion matrix, unseen 3 hp load [10]
actual
Normal
Inner race
Ball
Outer race
Normal
237
0
0
0
Inner race
0
216
21
0
Ball
0
0
236
0
Outer race
0
0
3
410
1,123 test windows. Confusions occur only between fault types, never between fault and healthy.
Already established
Industrial vibration sensors
Wireless gateways
OPC UA
CMMS APIs
ISO vibration guidance [5]
Still to be validated in the pilot
Real plant noise
Variable loading
Fault lead time
Sensor placement
False-alert rate
Model transfer
India Chem 2026 · NIT Warangal
5 / 8
Notes: How the detection works. A bearing defect makes the vibration signal impulsive and shifts energy into characteristic frequency bands. We compute sixteen standard indicators per window, things like RMS, kurtosis, crest factor and band energies, and a random forest classifies them. We trained and tested this ourselves on the public Case Western bearing dataset. Under a strict protocol, whole recordings held out and one motor load never seen in training, four-class accuracy is 97.9 percent, and none of the 237 healthy benchmark windows was misclassified. The confusion matrix shows the only errors are between fault types, not between faulty and healthy. And the caveat is printed on the slide: this is a controlled test rig with seeded faults, not a chemical plant. Sensors, gateways and integration standards are mature; what still needs proof is plant noise, lead time and false-alert rate, which is exactly what the pilot measures. About 75 seconds.

## Slide 6
Methodology for execution and way forward
Shadow-mode deployment validates alerts before maintenance teams rely on the system
Six-month pilot plan
M0
M1
M2
M3
M4
M5
M6
Baseline and asset selection
Sensor installation and integration
Commissioning and healthy baselines
Shadow-mode validation
go or no-go decision
Roles:
Reliability engineer: baseline, adjudication, gate · Instrumentation team: install · CMMS administrator: work-order flow · NAADI team: features, models, dashboards
Pilot success criteria
≥70%
of the faults maintenance later confirms must have been flagged by NAADI in advance
≥14 days
of notice: enough to plan the repair into a scheduled window instead of an emergency stop
≤2
false alerts per pump per month, so operators keep trusting the alerts
≥95%
sensor data availability
Alerts run in shadow mode for three months and are compared weekly with actual maintenance findings before any alert changes a maintenance decision.
Scale-up after the gate
Months 0 to 6
pilot: 25 pumps, one plant
Months 6 to 12
100 or more rotating assets: compressors, agitators, fans
Months 12 to 24
shared deployment across chemical clusters [3][4]
Pilot requirement
one plant partner · 25 critical pumps · historical CMMS data · six months of site access
India Chem 2026 · NIT Warangal
6 / 8
Notes: Execution is a six-month pilot with one principle: the system must earn trust before anyone relies on it. Months zero to one build the baseline from the plant's own maintenance records and fix the success criteria together with the plant, so the pass bar is agreed before installation. Month two is installation: wireless sensors magnet-mounted during routine access, no shutdown, permits handled through the plant's normal process. Month three commissions healthy baselines, and months three to six run in shadow mode: alerts are logged and compared weekly with what maintenance actually finds, but no decision depends on them yet. The month-six gate is numeric and is on the slide. In plain terms: of the faults maintenance later confirms, at least seven in ten must have been flagged by NAADI beforehand, with at least fourteen days of notice, which is enough to plan the repair into a scheduled window instead of an emergency stop. Alongside that, at most two false alerts per pump per month, and ninety-five percent data availability. Pass the gate and the system goes live, then scales to other rotating assets and, between months twelve and twenty-four, to a shared deployment across chemical clusters. What we need is one plant partner, the pumps, their history and six months of access. About 75 seconds.

## Slide 7
Economic feasibility and risks
The base case pays back in 11 months, with a 24-month downside case
₹37 lakh
estimated CapEx, 25 pumps
Team estimate
₹41.4 lakh
annual net benefit, base case
Team calculation
≈11 months
base-case payback
Team calculation
≈24 months
stacked-downside payback
Team calculation
Annual benefit build-up, INR lakh, base case
+39.4
Avoided downtime value [2]
+3.0
Repair savings [2]
+5.0
Avoided severe failures
-6.0
Annual OpEx
+41.4
Net annual benefit
downtime reduction taken at 35%, the low end of the DOE FEMP range [2]
Payback sensitivity, months
45% downtime reduction
8.4
Base case
10.7
CapEx plus 30%
14.0
Lost margin one-third lower
15.7
20% downtime reduction
18.1
Stacked downside
23.6
Key risks
impact ↑
likelihood →
1
2
3
4
1 False-alert fatigue
shadow mode first; at most 2 alerts per pump-month at the gate
2 Hazardous-area hardware
hardware meeting applicable PESO and IECEx requirements [6]
3 OT cybersecurity
one-way data flow on a segregated network; no path to the DCS
4 Few early failure examples
anomaly-first models per pump; classifier added as data grows
Environmental gains
Earlier detection of seal degradation can reduce leak-event risk [8]
The same condition data can identify cavitation and off-design operation; pumping is close to 20% of world electric-motor demand [9]
Recommendation: proceed with a six-month shadow-mode pilot, subject to plant-data validation and vendor quotations.
India Chem 2026 · NIT Warangal
7 / 8
Notes: The economics, with the calculation visible. Each avoided downtime hour is worth about 1.9 lakh of contribution margin. Taking the US Department of Energy's published effectiveness range at its low end, 35 percent downtime reduction and 10 percent repair savings, the waterfall builds to 47.4 lakh of annual benefit, less 6 lakh of operating cost, so 41.4 lakh net. Against an estimated 37 lakh of CapEx that is roughly an 11-month base-case payback and about 1.1 crore of five-year NPV at a 12 percent discount rate. The sensitivity chart stress-tests it: even if the programme delivers only 20 percent reduction, below the DOE band, or CapEx overruns by 30 percent, payback stays under 24 months in the stacked downside. The risks we take most seriously are false-alert fatigue, hazardous-area compliance, OT security and the shortage of early failure examples; each has a specific mitigation on the slide. Environmentally, earlier seal-fault detection reduces leak risk, and the same data helps find cavitation and off-design operation. Our recommendation is deliberately conditional: proceed with the pilot, subject to plant-data validation and vendor quotations. About 75 seconds.

## Slide 8
Supporting evidence
Sources, standards and calculation basis
Government and industry guidance
[1]
Department of Chemicals and Petrochemicals (GoI) and FICCI. Youth Innovation Challenge brief, India Chem 2026. 2026. Provided competition document.
[2]
US Department of Energy, FEMP. Operations and Maintenance Best Practices Guide, Release 3.0 (predictive maintenance chapter). 2010. energy.gov
[3]
NITI Aayog. National Strategy for Artificial Intelligence. 2018. And DST, National Mission on Interdisciplinary Cyber-Physical Systems. 2018. dst.gov.in
[4]
Ministry of Heavy Industries. SAMARTH Udyog Bharat 4.0 (Industry 4.0 centres). 2024. samarthudyog-i40.in
Engineering standards
[5]
ISO 20816-3:2022 machine vibration evaluation; ISO 13374-1:2003 condition-monitoring data processing; ISO 17359:2018 condition-monitoring guidelines; ISO 14224:2016 reliability data collection. iso.org
[6]
Petroleum and Explosives Safety Organisation (PESO), DPIIT. Statutory approvals for equipment in hazardous areas. peso.gov.in
Technical literature
[7]
Nowlan, F.S. and Heap, H.F. Reliability-Centered Maintenance. US DoD report AD-A066579. 1978.
[8]
McKee, K. et al. A review of major centrifugal pump failure modes. ICOMS Asset Management Conference. 2011. espace.curtin.edu.au
[9]
Hydraulic Institute, Europump and US DOE. Pump Life Cycle Costs: A Guide to LCC Analysis for Pumping Systems. 2001.
Dataset and team calculations
[10]
Case Western Reserve University Bearing Data Center, seeded-fault vibration dataset. Team model code train_fault_model.py and results metrics.json, 2026. Benchmark results only; not plant performance. engineering.case.edu/bearingdatacenter
[11]
Team economics: NAADI_pilot_economics.xlsx (live formulas and assumption register) and CALCULATIONS.md, 2026. Plant archetype values are team estimates pending pilot data.
Basis of preparation. Estimates and calculations are labelled where they appear. The comparison scores on slide 3 are team judgement. No plant trial, vendor quotation or primary research has been completed yet; the pilot in slide 6 is designed to supply that evidence.
India Chem 2026 · NIT Warangal
8 / 8
Notes: The reference slide groups everything we relied on: government guidance including the Department of Energy maintenance ranges, the engineering standards for vibration evaluation and reliability data, the technical literature behind the failure statistics, and our own dataset work and economics files. Numbers in square brackets throughout the deck point here. The basis-of-preparation note states plainly what is estimated, what is judgement and what has not yet been proven. We are happy to take questions. About 30 seconds.