## Slide 2
Recommendation: validate before selling. A 30-car hydrogen retrofit pilot in a captive Faridabad fleet, scaled only if delivered hydrogen falls below about ₹190 per kg
Answer to the brief: a CNG-to-hydrogen retrofit can be made safe by 2030, but at unsubsidised hydrogen prices it is not affordable; its 2030 role is a policy-supported niche of about 1,400 cars, not a mass product.
H₂-SHIFT
Convert. Don't Replace.
1. THE ANSWER TO THE BRIEF'S QUESTION
• Safe: yes, with known engineering (composite cylinder, thermally activated relief, twin leak sensors, lean burn with NOx control). But no approval route exists today for a hydrogen retrofit of a car; creating one is gate 1.
• Affordable: not by 2030. At ₹800/kg delivered (2028) the converted car costs ₹13.7/km all-in versus ₹5.2/km on CNG. Fuel parity with CNG needs ₹188/kg; the cheapest 2030 forecast found is about ₹360/kg delivered.
• Viable complement: only as a captive-fleet niche next to hydrogen hubs. A compact BEV bought in 2028 comes to ₹5.6/km including purchase, so BEVs stay the economic default for high-utilisation fleets.
• So the strategy is an option, not a launch: an HCNG step that needs no vehicle change, a bounded H2-ICE retrofit pilot that creates the approval route and the data, and a scale decision in 2030 against explicit price gates.
2. FIRST CUSTOMER AND USE CASE
• Donor: Maruti Suzuki Dzire Tour S CNG, 3 to 5 years old, factory bi-fuel; petrol stays as the automatic backup fuel.
• Fleet: captive, return-to-base institutional and contract fleets (PSU and corporate staff transport, airport contracts) in Faridabad, Delhi-NCR, running 150 to 210 km per day with two depot fills.
• Why here: IOCL R&D Faridabad hosts India's only car-capable hydrogen dispensing point, and the MNRE Sahibabad-Faridabad-Delhi hydrogen corridor (sanctioned March 2025) brings buses and trucks that a shared station needs.
• Why not Delhi app-cabs first: the 2023 aggregator scheme counts only electric cars toward onboarding ratios, and CAQM allows only CNG or EV new aggregator vehicles in NCR from January 2026. A hydrogen conversion earns no credit there.
• Second hub: Ahmedabad-Vadodara-Surat corridor (Gujarat funds 30 percent of the first 20 hydrogen stations).
3. HOW BIG, HONESTLY (bottom-up, 2030)
Step | Vehicles
CNG vehicles on road, Mar 2025 (all types) | 8,195,000
Passenger cars among them (estimate) | 4,507,250
Factory-fitted, boot cylinder, under 6 yr in 2028 | 2,253,625
In commercial or institutional fleets | 450,725
In cities with a hydrogen hub by 2030 | 180,290
Plausible early adopters (hypothesis) | 9,014
Station-limited capacity: 8 hubs x 174 cars | 1,394
Realistic converted fleet by 2030 | 1,394
Round 1 said 1,00,000 cars by 2030. Stations, not demand, set the ceiling: one 500 kg/day hub at 70 percent utilisation serves about 174 cars.
Customer demand is a hypothesis: no fleet interviews exist yet; Phase 0 buys 30 of them.
Same idea as Round 1: convert the installed CNG base, fleets first, aggregate hydrogen demand at hubs. What changed: pump price instead of production cost, petrol backup instead of a second cylinder, a station-limited rollout, and explicit stop rules.
Evidence labels used throughout: verified = external source in the register; model = workbook output; assumption = stated input range; target = proposed value requiring validation.
Sources: PNGRB/Vahan 81.95 lakh CNG vehicles, Aug 2025 [W3-S2]; Delhi aggregator scheme 2023 [W3-S17]; CAQM NCR direction [W3-S19]; IOCL Faridabad dispensing [W3-S46]; MNRE pilot routes, PIB 3 Mar 2025 [W3-S36]; Gujarat Green Hydrogen Policy [W4-S76]; CEEW 2025 delivered cost [W4-S22]; model workbook (TCO, Market).
2

## Slide 3
H2-ICE is the only conversion at conversion cost, but it carries the weakest fuel economics; a fuel-cell conversion costs as much as a new BEV
Matched criteria for the same donor and duty (Dzire Tour S CNG, 55,000 km per year, owner decision in 2028). Values are model outputs unless a source is named.
H₂-SHIFT
Convert. Don't Replace.
Criterion | H2-ICE retrofit (selected) | Fuel-cell conversion | New compact BEV (donor sold) | Continue on CNG
What changes | Cylinder, lines, injectors, ECU, sensors; engine and petrol system retained | Whole powertrain: stack, battery, motor, inverter, cooling, tank, controls | New vehicle; donor sold for about ₹3.5 lakh | Nothing
Cost to the owner | ₹3.2 lakh installed at 10,000/yr; ₹7.7 lakh in the pilot | ₹15 to 25 lakh pilot; ₹8 to 12 lakh at volume (estimate) | ₹10.5 lakh purchase (Tiago EV to Punch EV class) | 0
Energy cost per km, 2028 | ₹12.0 blended (hydrogen km ₹14.8 at ₹800/kg) | About half of H2-ICE per hydrogen km | ₹1.5 (depot and public mix) | ₹3.6
Range per fill or charge | 61 km on hydrogen plus 555 km on petrol | About 2x H2-ICE on the same tank | 187 to 260 km in real-world tests | About 250 km at 25 km/kg
Refuel or recharge time | 3 to 5 min (350 bar, non-cooled fill) | 3 to 5 min | About 1 h DC (10 to 80 percent); 6 to 8 h AC | 3 to 5 min plus queue
Peak power versus petrol | About 52 percent (lean burn); city duty | Restored by electric drive | Higher | About 85 percent
Tailpipe | Zero CO2 on hydrogen km; NOx must be controlled | Water vapour only | Zero | About 105 g CO2/km
Approval route today | None for retrofits; AIS-195 covers new H2-ICE vehicles | None; AIS-157 scope excludes retrofitted or converted FCEVs | Established | Established
Supplier readiness | Injectors, valves, regulators production-intent; car-size cylinders scarce | Imported stacks; no light-duty supply chain in India | Mature | Mature
WHAT GLOBAL EXPERIENCE TEACHES
• Captive fleets with depot fuelling survive: KEYOU truck conversions (Germany, 2024 to 2027 with Daimler), ULEMCo van conversions (UK), Toyota's hydrogen HiAce at its Altona depot (2024), NTPC Leh buses (80 kg/day, 350 bar).
• Retail light-duty networks retreat: Shell closed its 7 California car stations (Feb 2024); H2 Mobility closed 36 German car stations (2025); Stellantis cancelled its hydrogen vans (Jul 2025); Toyota sold 210 Mirai in the US in 2025.
• H2-ICE momentum is heavy-duty: JCB EU type approval (May 2025); Cummins B6.7H built in Jamshedpur for Tata trucks (Mar 2025); 70 MNRE pilot vehicles are buses and trucks, zero cars.
• Small-car hydrogen combustion is live but pre-commercial: Suzuki and AVL hydrogen Swift prototype (1.4 L direct injection, 100 kW, Vienna, May 2026); Suzuki hydrogen Burgman (2023, 2025). No company sells a passenger-car hydrogen conversion anywhere.
• Transfer to India: design for a depot, not a network; treat fuel price as the gating variable; borrow heavy-duty supplier parts; do not cite prototypes as proof of cost.
Selected route: H2-ICE with port injection, lean burn and automatic petrol fallback. It is the only architecture that is a retrofit in cost and scope; its case rests entirely on the delivered hydrogen price, so the pilot is designed to measure exactly that.
Sources: KEYOU, ULEMCo, Toyota Australia, NTPC [W3-S61, S63, S55, S44]; Shell, H2 Mobility, Stellantis, Toyota sales [W3-S65, S66, S64, S51]; JCB, Cummins, MNRE pilots [W3-S60, S59, S37]; Suzuki-AVL Swift (Fuel Cells Works, 7 May 2026), Burgman [W3-S58]; AIS-157 scope [W2-S11 and Scribd copy]; BEV data [W3-S27, S30]; fuel-cell conversion costs are estimates.
3

## Slide 4
What the retrofit changes: storage, fuel delivery, controls and safety are new; the engine, petrol system and body are retained (concept, to be verified by mock-up)
Donor: Maruti Suzuki Dzire Tour S CNG, 1.2 L K-series, 60 kW on petrol, 55 L steel CNG cylinder in the boot, 37 L petrol tank, 163 mm ground clearance (no under-floor cylinder option).
H₂-SHIFT
Convert. Don't Replace.
System architecture (schematic, not to scale). Green = new, blue = retained, grey = removed.
H35 receptacle, check valve, filter (new)
60 L composite cylinder, 350 bar, OTV with TPRD, boot frame (new)
316L high-pressure line, two-stage regulator (new)
Hydrogen rail and 4 port injectors (new)
1.2 L K-series engine, gearbox, three-way catalyst (retained)
Petrol tank 37 L and petrol injection (retained, automatic backup)
Hydrogen ECU: dual map, lambda 1.6 to 2.2, fallback logic, diagnostics (new)
Twin hydrogen sensors, boot vent fan, cabin warning, manual shut-off (new)
TPRD vent line to outside, sealed boot bulkhead (new)
Lean NOx trap provision and lambda sensor (new, if cycle test needs it)
55 L steel CNG cylinder, CNG regulator, rail, lines (removed, not reusable)
Cold plugs, PCV route, calibration (modified)
1.12 kg
usable hydrogen per fill (1.44 kg nominal at 350 bar, 85 percent fill, 20 bar residual)
61 km
range per fill at 1.85 kg/100 km; 105 km with a 700 bar cylinder of the same size
~121 km/day
on hydrogen with two depot fills (73 percent of a 167 km day); petrol covers the rest
42 PS
peak power in hydrogen mode, 48 percent below petrol; city duty, automatic petrol switch at high load
-13 kg
net kerb mass change; cylinder is 84 mm larger in diameter, so the boot loses a further 40 to 60 L (estimate)
3 days
conversion downtime per car in the pilot; 14 labour hours at volume
Retained | Modified | Removed (cannot be reused with hydrogen) | Added
Engine, gearbox, body, brakes, suspension, petrol tank and injection, three-way catalyst, CNG-hardened valve seats | Calibration (lean lambda 1.6 to 2.2, retarded spark, injection timed after intake valve closing to stop backfire), cold-grade plugs, crankcase ventilation, boot bulkhead sealing and ventilation | 55 L steel CNG cylinder (ISO 11439 steel is limited to 2 percent hydrogen), CNG regulator, rail, injectors, hoses and lines | Composite cylinder (60 L, OD 400 x 767 mm, 36 kg), on-tank valve with TPRD, H35 receptacle, 316L lines, two-stage regulator, hydrogen injectors and rail, hydrogen ECU, two sensors, vent fan, lean NOx trap provision
Injection strategy: port injection with late timing and lean mixtures avoids backfire and pre-ignition but costs power; direct injection (as in the Suzuki-AVL Swift prototype) recovers it but is not a retrofit. Durability items to prove: valve seats and guides, lubricant ash, sensor drift. Consumption cross-check: 1.85 kg/100 km equals 0.87 of the CNG car's energy efficiency at 25 km/kg.
Sources: Maruti Suzuki Tour S and Dzire specifications [W1-S3a to S3c]; Luxfer G-Stor Pro V060H35 [W1-S2]; hydrogen densities 24.0 and 40.2 g/L at 15 C [W1-S13a]; PFI power loss and lambda-NOx behaviour [W1-S9a, S9b, S9h]; ISO 11439 hydrogen limit [W1-S11a]; UN R110 20 g / 8 g mounting loads [W1-S14d]; model workbook (Energy_Range, BOM).
4

## Slide 5
Safety: the hazards are known and controllable; approval is the real gap, because no route exists yet for a hydrogen retrofit of a car
Hydrogen ignites between 4 and 75 percent in air at 0.017 mJ, diffuses 3.8 times faster than natural gas and burns almost invisibly: different risks, not automatically higher, if designed for.
H₂-SHIFT
Convert. Don't Replace.
Hazard | Prevention (design) | Detection and response | Validation evidence
Leak into boot, cabin, garage or basement | Sealed boot bulkhead, vented boot, no ignition sources in the bay, valve closed when engine off | Two hydrogen sensors (alarm at 1 and 2 percent), tank valve closes within 1 s, ECU switches to petrol, driver warning | Concentration below 4 percent in cabin and below 8 percent at vents (GTR 13 / AIS-195 type tests); enclosed-space test
Embrittlement, permeation, material ageing | Hydrogen-rated 316L lines, elastomers and composite liner; no reuse of CNG steel parts | 3-yearly cylinder requalification (Gas Cylinder Rules 2025), 15-year life, leak check at service | Supplier qualification to ISO 19881 / UN R134; cycling and permeation tests
Crash damage | Cylinder behind rear seat inside the crush-free zone; frame designed to 20 g / 8 g loads | Inertia switch closes the tank valve; post-crash leak limit | Sled test of the mounting, full-vehicle rear crash under AIS-195 procedures
Overpressure and fire | TPRD vents away from occupants, wheel wells and electrics; burst ratio 2.25 x working pressure | TPRD opens on heat; controlled release rather than rupture | Bonfire, burst, drop and cycling tests (GTR 13); vent-line routing review
Detection or control failure | Redundant sensors, ECU watchdog, manual shut-off valve, limp-home on petrol | Fault codes, forced petrol mode, service lock-out | Hardware-in-the-loop and fault-injection tests; 500 h engine durability
Workshop and refuelling incidents | NFPA 2 type ventilation (1 cfm per sq ft), hydrogen detection, permit-to-work, PESO-trained staff | Gas detection interlocks on the dispenser and in the bay; nitrogen purge for venting | PESO Form-H licence for the dispensing point; SAE J2601 fill protocol; lessons from Kjørbo 2019 (assembly error) and Santa Clara 2019 (procedures)
APPROVAL PATH AND OPEN QUESTIONS
• Exists: AIS-195:2023 (Amd 1, May 2025) for new M and N hydrogen ICE vehicles via CMVR Rule 125M (GSR 746(E), 16 Oct 2023).
• Exists in principle: MV Act s.52 and CMVR Rule 126 proviso (retrofitted vehicles tested and type-approved by test agencies) plus the Rule 115 CNG-kit machinery: kit type approval, authorised workshops, RC endorsement (Form 22D).
• Gap: no hydrogen retrofit kit standard or emission procedure; AIS-157 explicitly excludes retrofitted or converted fuel-cell vehicles; the AIS-195 position on retrofits could not be verified (document inaccessible in this study).
• Cylinders and stations: Gas Cylinder Rules 2025 now cover on-board hydrogen cylinders; PESO Form-H licences for dispensing online since May 2025; no car-size PESO-approved cylinder yet.
• Trial route: trade certificate plus test-agency evaluation, as used for the ICAT Mirai pilot (2022) and the Tata truck trials (2025); the MNRE transport pilot scheme names 4-wheelers.
• Insurance and warranty: IMT-25 covers only CNG and LPG kits; OEM warranty is void after conversion. Both need new instruments.
NOx: hydrogen combustion still forms thermal NOx (US DOE). Lean burn above lambda 2 keeps engine-out NOx near zero at steady state, but accelerations leave that regime, so the design carries a lean NOx trap provision and must meet BS-VI 60 mg/km on the certification cycle. This is a target to demonstrate, not a result.
We do not claim 'approved' or 'fully safe'. Gate 1 (March 2027): a written regulator and test-agency view on the retrofit route, or the programme stops.
Sources: H2Tools hydrogen properties [W2-S43]; DOE 'Similar but Different' [W2-S44]; NFPA 2 [W2-S45]; GTR 13 limits [W2-S42]; Gas Cylinder Rules 2025, GSR 225(E) [W2-S24]; PESO Form-H [W2-S27]; GSR 746(E) Rule 125M [W2-S13]; Rule 126 and Rule 115 [W2-S9, S3]; AIS-157 scope [W2-S11, Scribd copy]; IMT-25 [W2-S53]; incidents [W2-S48, S49]; DOE NOx page [W2-S52].
5

## Slide 6
Economics: at every credible hydrogen price to 2032 the retrofit costs the owner more than staying on CNG; the sign never turns
Fair comparison for an owner deciding in 2028 with a 3-year-old Dzire Tour S CNG: keep it, convert it, or sell it and buy a compact BEV. Five years, 55,000 km per year, 12 percent discount rate, unsubsidised, same time costs for queues and charging.
H₂-SHIFT
Convert. Don't Replace.
Chart: Cost per km, base case (model)
| Continue on CNG | Hydrogen retrofit | Sell, buy compact BEV
Fuel or energy, ₹/km (2028) | 3.65 | 12 | 1.53
All-in levelised cost, ₹/km | 5.25 | 13.73 | 5.55
Five-year NPV of costs: continue ₹10.4 lakh; retrofit ₹27.3 lakh; BEV ₹11.0 lakh (donor sale of ₹3.5 lakh and BEV resale credited).
Hydrogen at ₹800/kg in 2028 falling 10 percent a year; CNG ₹87/kg; petrol ₹102/L; depot power ₹6/kWh, public DC ₹20/kWh.
Condition for competitiveness | Value (model)
Fuel-cost parity with CNG (₹/kg delivered) | ₹188
Fuel-cost parity with petrol (₹/kg) | ₹368
Full-TCO break-even versus continuing on CNG | None within 5 years at any hydrogen price: kit cost and petrol backup km outweigh the fuel saving
Full-TCO break-even versus the BEV | None at base; needs hydrogen below about ₹150/kg with a ₹2 lakh kit and 85 percent hydrogen km
Conversion cost | ₹7.7 lakh pilot; ₹3.2 lakh installed at 10,000/yr (₹2.3 lakh ex-works). Round 1 said ₹1.8 to 2.2 lakh
Extra cost of converting versus continuing (5 yr) | ₹16.8 lakh at base; ₹5.8 lakh even at ₹250/kg hydrogen
Abatement cost versus continuing | ₹129,000 per t CO2e at base; about ₹45,000/t at ₹250/kg (India voluntary credits trade at ₹1,350 to 2,800/t)
Extra cost of the retrofit versus continuing on CNG over 5 years, ₹ lakh (model)
₹/kg \ km/yr | 30,000 | 50,000 | 70,000
₹150 | +3.6 | +3.8 | +4.0
₹250 | +4.7 | +5.6 | +6.5
₹400 | +6.3 | +8.3 | +10.3
₹600 | +8.5 | +11.9 | +15.4
₹800 | +10.7 | +15.6 | +20.5
Every cell is positive: the conversion never saves money against CNG in this horizon. Higher mileage makes it worse while hydrogen is dearer than ₹188/kg.
Against a petrol-only donor, fuel parity sits at ₹368/kg, inside the 2030 forecast range, but a ₹60,000 CNG conversion beats it wherever CNG exists. LNG passenger cars do not exist in India.
Reading: the retrofit is a decarbonisation cost, not a saving. It needs a paying counterparty (policy or a corporate abatement budget) or a far cheaper hydrogen molecule than any 2030 forecast found (CEEW ₹360/kg delivered; record refinery-gate tender ₹279/kg before compression and dispensing).
Sources: CNG and petrol prices Sep 2026 [W4-S16, S19]; DERC EV tariff and public charging [W4-S20, S21]; BEV prices and tests [W3-S27, S30]; battery warranties and degradation [W4-S26, S27]; NITI Aayog taxi mileage [W4-S30]; CEEW 2025 delivered hydrogen [W4-S22]; Numaligarh tender ₹279/kg [W3-S39]; carbon credit prices [W4-S73]; model workbook (TCO, Sensitivities, BOM).
6

## Slide 7
Fuel supply: a 30-car pilot needs about 60 kg a day; delivered hydrogen costs about ₹1,433/kg at a pilot point and about ₹584/kg at a 2030 hub at 70 percent utilisation
Pilot setting: Faridabad, Delhi-NCR. IOCL R&D dispensed hydrogen for the 2022 Mirai pilot and its fuel-cell buses; the MNRE Sahibabad-Faridabad-Delhi corridor was sanctioned in March 2025 (18 to 24 months to commission). No station is public or confirmed available: access is a proposed partnership.
H₂-SHIFT
Convert. Don't Replace.
Chart: Delivered price build-up, unsubsidised (model): ₹1,433 pilot, ₹584 hub
| Pilot point 2028 (150 kg/day, 50 percent used) | Hub station 2030 (500 kg/day, 70 percent used)
Production (green, plant gate) | 400 | 240
Tube-trailer transport | 45 | 45
Compression electricity | 27 | 27
Station capital recovery | 646.5175 | 166.2474
Station O&M | 146.1187 | 37.5734
Losses, margin, taxes | 168.1966 | 68.6042
Production ₹400/kg (2026-28) and ₹240/kg (2030) from CEEW, IEA and SIGHT auction evidence; capex ₹10 crore (pilot) and ₹12 crore (hub) recovered over 10 years at 12 percent. CEEW's central 2030 case is ₹360/kg at a 1,000 kg/day station; ours is deliberately conservative.
Station sizing from the fleet (pilot) | Value
Cars x km/day x kg/km | 30 x 167 x 0.0185 x 0.65 share = 60 kg/day
Fills per day; peak-window rate | 60 fills; 10 per hour in a 3 h start-of-shift window
Dispenser positions (6 fills/h each) | 2
Compressor throughput (16 h/day, 150 kg/day design) | 9.4 kg/h
Cascade storage buffer (1.5 days) | 90 kg at 450 bar
Tube-trailer deliveries (300 kg payload) | 1.4 per week
Utilisation from cars alone; assumed with bus and truck users | 40 percent; 50 percent
Planned downtime, supply interruption cover | Buffer covers 1.5 days; petrol backup covers the rest
Cars one 2030 hub can serve | 174 at 70 percent utilisation
WHO DOES WHAT (proposed, not committed)
• Vehicles: fleet partner owns and operates; programme buy-back guarantee on residual value.
• Kits: SRDI-led consortium owns during the pilot; kit integrator warrants parts and workmanship.
• Station: oil marketing company partner (proposed IOCL, Faridabad) owns and operates under a PESO Form-H licence; take-or-pay from the fleet covers utilisation risk.
• Fuel: certified green hydrogen (2 kg CO2e/kg standard) by tube trailer from a SIGHT-awarded producer; delivered price is a programme cost during the pilot.
• Service: two hydrogen-ready workshops with trained staff; 3-yearly cylinder tests at a PESO-approved station.
• Risk carriers: development (programme); utilisation (station partner with take-or-pay); residual value (fleet, backed by buy-back).
Utilisation alone cannot close the gap: at 95 percent utilisation the hub price is still about ₹524/kg, and CNG parity (₹188/kg) is out of reach because production, transport and compression alone exceed it. Delivered versus on-site electrolysis: delivered hydrogen keeps the pilot's capital to a dispensing point; an electrolyser is justified only at hub scale.
Sources: MNRE pilot corridors, PIB 3 Mar 2025 [W3-S36]; IOCL Faridabad dispensing [W3-S46, W4-S81]; CEEW 2025 station model [W4-S22]; ICCT station cost by utilisation [W4-S46]; Indian station capex indication [W4-S56]; green hydrogen cost evidence [W4-S33, S38, S57]; Gas Cylinder Rules and Form-H [W2-S24, S27]; model workbook (H2_Supply).
7

## Slide 8
Roadmap to 2030: four gated phases, ₹37.6 crore including contingency, with a proceed, redesign or stop decision at each gate
Calendar phases from October 2026; each phase ends with evidence, not a date. Suzuki R&D Center India is proposed as engineering lead; public support is sought under the MNRE transport pilot scheme, which names 4-wheelers.
H₂-SHIFT
Convert. Don't Replace.
PHASE 0 Oct 2026 to Mar 2027
Feasibility and validation | ₹0.9 cr
PHASE 1 Apr 2027 to Mar 2028
Engineering and controlled validation | ₹8.5 cr
PHASE 2 Apr 2028 to Mar 2029
Certification and pilot build | ₹15.2 cr
PHASE 3 Apr 2029 to Sep 2030
Pilot operation and evaluation | ₹8.1 cr
PHASE 4 from Oct 2030
Expansion only if gate 4 passes | conditional
 | Phase 0 | Phase 1 | Phase 2 | Phase 3 | Phase 4 (conditional)
Deliverable | Written regulator and test-agency view on the retrofit route; 30 fleet interviews and telematics on 20 cars; boot mock-up and CAD packaging; station partner letter | 500 h hydrogen engine test-cell programme; 3 converted prototypes; storage qualification (burst, cycling, bonfire, drop); vehicle leak, ventilation and crash-structure tests | Kit type approval under the agreed route; 80,000 km durability on 2 cars; 30 conversions; dispensing point commissioned; 2 workshops upgraded | 18 months of operation with 10 CNG and 10 BEV comparison cars; quarterly emission tests; independent evaluation report | 1,000 to 1,500 cars at up to 8 hub stations; localised cylinders and kit production
Accountable | SRDI engineering lead; ARAI or ICAT; PESO liaison | SRDI with a test-cell partner (HORIBA Chakan or ARAI); cylinder supplier | Kit integrator; ARAI or ICAT; OMC station partner; fleet partner | Fleet partner operations; independent evaluator (IIT or CEEW); SRDI data team | Consortium and public programme
Dependencies | Regulator engagement; fleet access | Car-size cylinder samples (Luxfer, Quantum, NPROXX, Time Technoplast); hydrogen injectors | MNRE pilot sanction; PESO approvals; corridor station timing | Fuel supply contract; insurer endorsement | Delivered hydrogen price; policy support
Gate and decision | Gate 1: route defined, partner secured, demand evidence from 3 fleets. Otherwise stop. | Gate 2: consumption at or below 2.2 kg/100 km, NOx at or below 60 mg/km on cycle, no abnormal combustion in 500 h, safety tests passed. Otherwise redesign once, then stop. | Gate 3: approval granted and station commissioned within 6 months of plan. Otherwise pause. | Gate 4 (Sep 2030): availability 95 percent or better, zero reportable hydrogen incidents, measured ₹/km published, delivered hydrogen at or below ₹250/kg with a credible path to ₹190/kg. Otherwise stop and publish. | Proceed only with fuel price and approval in place
Proposed funding split (not committed) | Share | ₹ crore
Suzuki R&D Center India and Maruti Suzuki: engineering, prototypes, test cells | 40 percent | 15.0
Public support sought: MNRE transport pilot scheme (4-wheelers named) or R&D scheme, state hydrogen policy | 35 percent | 13.1
Oil marketing company partner: dispensing point | 15 percent | 5.6
Fleet partner: vehicles, drivers, operations | 10 percent | 3.8
Total to September 2030 (incl. 15 percent contingency) | 100 percent | 37.6
Why Suzuki's role is plausible: CNG engine and calibration know-how, a 70 percent share of India's CNG cars, and its own hydrogen combustion work (Swift prototype with AVL, 2026; Burgman). This is a proposal; no endorsement is implied.
Sources: MNRE scheme guidelines, PIB 14 Feb 2024 (buses, trucks and 4-wheelers) [PIB PRID 2006052]; ARAI Phase-II call for proposals (Sep to Dec 2025); HORIBA and ARAI hydrogen test facilities [W4-S14, S15]; CNG kit approval precedent [W2-S3, S8]; PESO rules [W2-S24]; model workbook (Pilot_Budget).
8

## Slide 9
Expected impact is real but small by 2030; the decision requested is ₹0.9 crore for Phase 0, which buys the facts that decide whether ₹37.6 crore is worth spending
Bounded outcomes at matched service (same car, same duty), with the assumptions under which each conclusion reverses.
H₂-SHIFT
Convert. Don't Replace.
Chart: Emissions per km, same car and duty (model)
| Continue on CNG | Retrofit, green H2 | Retrofit, grey H2 | BEV, 2025 grid | BEV, 2030 grid
g CO2e per km, well-to-wheel incl. amortised manufacturing | 137 | 89 | 208 | 176 | 134
Green-hydrogen retrofit: 35 percent below CNG (petrol backup km included). Grid-electrolysis hydrogen would be 533 g/km, four times worse than CNG. Reversal thresholds: hydrogen above 5.9 kg CO2e/kg makes the retrofit worse than CNG; grid below 0.29 kg/kWh at the meter makes the BEV cleaner than the green-hydrogen retrofit (CEA path reaches about 0.5 by 2032).
NOx is the other tailpipe issue: zero CO2 on hydrogen km does not mean zero pollutants.
Bounded outcome | Pilot (30 cars) | 2030 conditional (about 1,400 cars)
CO2e avoided per year (green hydrogen) | 78 t | 3,645 t
Hydrogen demand per year | 20 t | 924 t (about one hub station)
Conversion kits sold | 30 (₹7.7 lakh each) | about 1,400 (₹3.2 lakh each, ₹45 crore)
Round 1 claim for 2030 |  | 1,00,000 cars; 0.9 Mt CO2; 15,000 t/yr hydrogen
TOP REMAINING UNCERTAINTIES (ranked)
• 1. Delivered hydrogen price: ₹360 to ₹1,430/kg across sources and our build-up; the single variable that decides everything.
• 2. Approval route: none exists; timing depends on AISC, MoRTH and PESO.
• 3. NOx on transients: lean burn is clean at steady state only; aftertreatment and cycle results pending.
• 4. Car-size cylinder supply and PESO approval: only 150 to 250 L truck cylinders approved in India so far.
• 5. Customer demand: a hypothesis until Phase 0 interviews; power loss and boot loss may be refused.
DECISION REQUESTED
• Approve Phase 0 (₹0.9 crore, six months) and the four-gate framework; no commitment beyond gate 1.
• Endorse an application under the MNRE transport pilot scheme (4-wheeler category) with ARAI as implementing agency, and a Gujarat hydrogen-station subsidy request for the second hub.
• Nominate an SRDI engineering lead and a fleet and fuel partner shortlist (proposed: IOCL Faridabad, PSU and airport-contract fleets).
• Start the HCNG step in parallel where a CGD company can blend to IS 17314: legal since 2020, no vehicle change, about 6 percent of energy from hydrogen, an air-quality measure rather than a decarbonisation step.
• What would make us stop: no regulator route by March 2027; NOx or backfire not controlled in 500 h; delivered hydrogen still above ₹250/kg with no path to ₹190/kg in 2030; fleets unwilling to accept a 48 percent power loss and a smaller boot.
H2-SHIFT keeps India's hydrogen retrofit option open at low cost, tells the truth about price, and hands the 2030 scale decision to evidence instead of ambition.
Sources: CEA CO2 baseline v21 and National Electricity Plan [W4-S59, S60]; IPCC fuel factors [W4-S62]; ICCT 2025 lifecycle factors and battery footprint [W4-S63]; hydrogen carbon intensities [W4-S64, S65]; DOE NOx page [W2-S52]; MNRE scheme scope, PIB 14 Feb 2024; Gujarat policy [W4-S76]; H-CNG notification GSR 585(E) [W2-S1]; model workbook (Emissions, Market, Pilot_Budget).
9

## Slide 10
Key sources and annexure index
Research cut-off 14 September 2026. Full register of 300 plus entries with URLs, dates, sections and limitations is in the annexure and the workbook (Sources sheet).
H₂-SHIFT
Convert. Don't Replace.
1. PIB, MNRE, 'Pilot Projects on Hydrogen Fuelled Buses and Trucks Launched under the NGHM', 3 Mar 2025 (PRID 2107795): 5 projects, 37 vehicles, 9 stations, 10 routes incl. Sahibabad-Faridabad-Delhi, ₹208 crore.
2. PIB, MNRE, 'Scheme Guidelines for Pilot Projects on use of Green Hydrogen in the Transport Sector', 14 Feb 2024 (PRID 2006052): buses, trucks and 4-wheelers; ₹496 crore; PIB 29 Jul 2026: 12 projects, 70 vehicles, 16 stations, ₹410.77 crore.
3. MoRTH, GSR 746(E), 16 Oct 2023: CMVR Rule 125M, AIS 195:2023 for hydrogen ICE vehicles of categories M and N; ARAI AIS-195 with Amendment 1 (May 2025); AIS 157:2020 (GSR 579(E), 23 Sep 2020), scope excludes retrofitted or converted fuel-cell vehicles.
4. DPIIT/PESO, Gas Cylinders (Amendment) Rules 2025, GSR 225(E), 11 Apr 2025: on-board hydrogen cylinders, 3-yearly testing, 15-year life; PESO Form-H online licensing for hydrogen dispensing, May 2025.
5. MoRTH, GSR 585(E), 25 Sep 2020: H-CNG per IS 17314:2019 added to CMVR Rule 115; IOCL and DTC 50-bus HCNG trial, Oct 2020.
6. PNGRB citing Vahan (Aug 2025): 81.95 lakh CNG vehicles (Mar 2025); MoPNG: 8,150 plus CNG stations, 17,700 to 18,000 targeted by 2030; IGL, MGL, MNGL price notices Sep 2026.
7. Maruti Suzuki specifications and releases (Tour S, Dzire, WagonR, Ertiga, Eeco); Maruti CNG sales FY25 6.12 to 6.2 lakh, FY26 above 7 lakh; Suzuki Growth Strategy FY2030.
8. Luxfer G-Stor Pro H2 specification table (V060H35: 60 L, 350 bar, 36 kg, 1.45 kg); Hexagon Purus Type 4 table (Rev 08/22); US DOE Records 19008 and 24006 on Type IV storage cost.
9. US DOE and H2Tools: hydrogen properties; 'Does the use of hydrogen produce NOx'; NFPA 2 (2023); UN GTR 13 Amendment 1 (2023) and UN R134; SAE J2601 (2020); ISO 19881:2025; ISO 14687.
10. CEEW (2025) India hydrogen and EV TCO model: delivered green hydrogen USD 4.2/kg in 2030; ICCT (2022, 2025): station cost by utilisation, lifecycle factors; IEA Global Hydrogen Review 2025; NITI Aayog (Feb 2026) taxi mileage 70,000 km/yr.
11. CEA CO2 Baseline Database v21 (FY2024-25, 0.710 t/MWh) and National Electricity Plan 2022-32; IPCC 2006 fuel factors; MNRE Green Hydrogen Standard (2 kg CO2e/kg).
12. Global programmes: Toyota (Mirai, HiAce, GR Corolla), Hyundai Nexo, KEYOU, ULEMCo, JCB, Cummins B6.7H India, Stellantis (Jul 2025), Shell California (Feb 2024), H2 Mobility Germany (2025); Suzuki-AVL hydrogen Swift, Vienna Motor Symposium, May 2026 (Fuel Cells Works, RushLane).
13. Delhi Motor Vehicle Aggregator and Delivery Service Provider Scheme 2023; Delhi EV Policy 2026; CAQM NCR direction (Jan 2026); Gujarat Green Hydrogen Policy 2025; Maharashtra Green Hydrogen Policy 2023.
ANNEXURE INDEX (separate PDF and workbook)
A1 Claim audit: Round 1 versus evidence, with corrections
A2 Assumptions, evidence classes and full source register
A3 Cost model: BOM, TCO, break-even, sensitivities
A4 Packaging, energy balance and performance calculations
A5 Regulatory compliance matrix and hazard analysis
A6 Market sizing method and bottom-up funnel
A7 Global benchmark evidence (progress and setbacks)
A8 Pilot design, instrumentation and first 90 days
A9 Phase budgets, responsibilities and funding
A10 Judge Q&A, validation log and change log
Workbook: H2SHIFT_model.xlsx (11 sheets, formula-driven, recalculated)
Evidence discipline: every headline number traces to a source ID (verified), a workbook cell (model) or a stated assumption. Many original documents were inaccessible through the build environment's network policy; such entries are marked 'excerpt' or 'summary' in the register and should be re-verified before external use. No customer interviews, letters of interest, test results or partnerships are claimed.
Team Wookies, NIT Warangal. SRDI Igniters Innovation Challenge 2026, Engineering Track, Option 2: Hydrogen Retrofit Solution. Round 2 submission.
10